## Slide 1: GE8291 Environmental Science and Engineering
Rajasekaran S
Assistant Professor,
Department of Information Technology,
KGiSL Institute of Technology,
email: proffraja@gmail.com
Github:www.github.com/rajasekaranap

## Slide 2: Air Pollution
Photochemical Reaction
  Components of atmosphere is react with one another with a presence of sunlight to introduce another components is known as photochemical reaction.
  Eg:
NO2
HNO3
Moisture
hv

## Slide 3: Air Pollution
Formations of smoke:
  Brownish smoke appeared in large cities in the presence of sunlight.
  It is visible only in noon time

## Slide 4: Air Pollution
Source:
  Unburnt fuel exhausted from vehicle and it reacts with oxides of nitrogen in the presence of sunlight.
  Produces secodanry polutants like peroxyacyl nitrate, ozone, aldehydes and ketones.
Effect:
  Breathing problems, eye, nose and throat irritation, Heart desseies.

## Slide 5: Air Pollution
Control of photochemical smog:
  Removing components of oxides of nitrogen by using compression or absorption techniques.
  It can be controlled by recycling hydrocarbons emitted from the vehicles.

## Slide 6: Oxygen and Ozone
Ozone is a allotropic from of oxygen.
Ozone contains 3 molecules.
In stratosphere continuously created by UV rays.
  O2 + hϒ  O + O
  O + O2 + hϒ  O3
  O3 + hϒ O2 + O
Net result is equilibrium concentration of ozone.

## Slide 7: Oxygen and Ozone
The equilibrium is disturbed by chlorine, bromine ... etc.
It destroys ozone molecules and result into thinning of ozone layer it known as ozone hole.
The process of creation of hole in ozone layer due to chloro fluro carbons and nitrous oxide in the stratosphere is called ozone layer depletion.

## Slide 8: Ozone Layer Depletion
Propellant in aerosol spray cans.
Refrigerants in refrigerators that contains freon gas.
High flying supersonic jets.
The detonation of nuclear weapons.
Blowing agent.
Usage of fire extinguisher.

## Slide 9: Ozone Layer Depletion
Depleting Substances:
  Freon – 11
    Banned in many countries.
  Freon – 12
    It is still used in refrigerators, air conditioners and freezers.
  Bromo fluoro carbons (BFC)

## Slide 10: Ozone Layer Depletion
Depleting Reaction:
  Step 1: Photo dissociation of Freon 12
    CCl2F2 + hϒ  CClF2 + [CL]
  Step 2: Ozone depletion or hole formation
    [Cl] + O3  ClO + O2
    ClO + [O]  [Cl] + O2
    ClO + O3  ClO2 + O2
  Aircrafts and jets produces NO
    NO + O3  NO2 + O2
    NO + O3  NO2 + [O]

## Slide 11: Ozone Layer Depletion
Effects of ozone layer depletion:
  It increases the UV light penetration that causes skin burns and skin cancer, kills lower fauna and flora.
  It affects photosynthesis process of plants.
  It also affects the climate change.
  Yield of vital crops like corns, rice, soybean, bean, cotton and wheat will decrease.
  Degradation of paints, plastics and other polymer materials will results in economic loss.
  UV rays affect the aquatic life.

## Slide 12: Ozone Layer Depletion
Control measures
  Controlling CFC release.
  Manufacturing of CFC is avoided.
  Research alternatives for CFC.
  Use of methyl bromide should be controlled.

## Slide 13: Acid Rain
Acid rain means the presence of excessive acid in rain water.
If the pH of rainwater is low (below 6.5) due to the presence of CO2, SO2 and NO2 gases in the atmosphere then the rain is called acid rain.
  CO2 + H2O  H2CO3
  SO2 + H2O  H2SO4

## Slide 14: Acid Rain
Effects of acid rain:
  Decay of building which are made up of marble.
  Damage of stone stages.
  Damages metals and car finishes.
  Aquatic life especially fish affected by the acidifications.

## Slide 15: Acid Rain
Control of acid rain:
  Emission of SO2, CO2 and NO2 should be controlled.
  Coal with lower sulphur content must be used for thermal power plants.
  Use of natural gals instead of coal.
  Liming of lakes and soils should be done to minimize the effects of acid rain.
  Coating of protective layer of inert polymer should be given in the interior water pipes of drinking water.
  Avoiding the unnecessary usage of motor vehicles.

## Slide 16: Global Warming
Green house effect or global warming is defined as “the progressive increase in earth’s temperature due to the effect of increase in composition of man-made CO2 in the atmosphere”.
Major greenhouse gases
  CO2, CH4, N2O, CFC ... etc

## Slide 17: Global Warming
Causes
  Industrialization
  Transportation
  Combustion of fossil fuel
  Deforestation

## Slide 18: Global Warming
Impacts
  Earth’s temperature increase from 1.5 ℃ to 5.5 ℃ by 2050.
  Melting of polar ice leads to sea water level increase.
  Change of rainfall pattern lead to spread of water borne diseases.
  Leading to drought and flood causes water demand.
  Species extinction due to rapid changes.

## Slide 19: Global Warming
Control Measures
  Reduce usage of CFC.
  Use of energy effectively.
  Use of renewable energy.
  Shift of coal to natural gas.
  Adopt sustainable agriculture.
  Stabilize the population growth.

## Slide 20: Particulate Matters
Particulate matters is a suspended droplets (or) solid particles or mixture of these two. It consists of inert or reactive materials is a size from 100 µ m.
Types
  Inorganic dust (iron dust).
  Droplets (Mist).
  Fly ash (coal combustion).
  Organic matters (benzene).

## Slide 21: Particulate Matters
Effects
  Petroleum combustion particles affects the haemoglobin formation.
  Fly ash – respiratory problems
  Metal dust - respiratory problems
  Aerosols by airplanes – depletion of ozone layer.
  Smog – effects on man and animal, cracks the rubber.
  Dust coating – in effect photo synthesis.

## Slide 22: Particulate Matters
Control Measures
  It should be controlled at source.
  Sedimentation.
  Centrifugation.
  Impaction.
  Filtration.
  Electrostatic precipitators.

## Slide 23: Oxides of Nitrogen (NOx)
NO forms and forms .
Sources
  Fuel combustion.
  Lightening.
  Forest fire.
  Decomposition of organic matters.

## Slide 24: Oxides of Nitrogen (NOx)
Effects
  It combined with haemoglobin and affects.
  is more toxic than NO affects the lungs and high concentration causes bronchitis (inflammation of the bronchi).
Control
  Modification of combustion conditions helps to reduces the NO levels.
  Usage of NO controlling devices.

## Slide 25: Carbon Monoxide
Effects
  It affects the haemoglobin.
  Head aches and anaemia.
Control
  Adsorption
  Absorption
  Condensation
  Combustion
  Source control

## Slide 26: Carbon Monoxide
It is colourless and odourless gas and poisonous to air-breathing animals.
2C
2C
Sources
  Cigarette smoking.
  Forest fire.
  Coal mines.
  Gas heaters.
  Incomplete combustion of fossil fuel.

## Slide 27: Sulphur Dioxides
It is colourless odourless irritating gas.
Sources
  Fossil fuels
Effects
  Breathing problem
  Irritates the lungs.
Control
  Burning fuel with less sulphur.
  Liquefying coal and other sulphur contain fuels.

## Slide 28: Hydrocarbons
It is produced in the atmosphere in the presence of sunlight and nitrogen.
Sources
  Fossil fuels.
Effects
  Irritates the eyes.
  Damage the lungs.
  Aggressive respiratory problems.
Control
  It can be reduced by fixing catalytic convertors in the exhaust pipes in automobiles.
  Controlling emission of hydrocarbons at the sources.

## Slide 29: Water Pollution
Water pollution is defined as the discharging of impurities to water which alter physical, chemical or biological properties and make it unfit for drinking and domestic purpose.
Sources
  Point sources.
  Non point sources.

## Slide 30: Water Pollution
Point Sources
  It are specific sites which directly discharge effluents to water bodies.
    Mining
    Iron and steel
    Chemical plants
    Soap and detergents
    Food processing
    Paper and in the pulp effluents

## Slide 31: Water Pollution
Non Point Sources
  It is not specific sites which are scattered.
    Surface runoff by agriculture.
    Municipal drainage overflow.
    Rain water sweeping the roads.

## Slide 32: Common Water Pollutants
Industrial waste [effluents of industry]
  Inorganic pollutants
    Water soluble.
    sulphates, cyanides, cadmium.
  Organic pollutants
    Cellulose fibbers.
    Oils, Fats, Phenols.

## Slide 33: Common Water Pollutants
Community waste or Domestic waste
  Agricultural sources
  Oil
  Waste heat
  Mining
  Air pollution
  Ground water pollution.

## Slide 34: Thank You
Rajasekaran S
Assistant Professor,
Department of Information Technology,
KGiSL Institute of Technology,
email: proffraja@gmail.com
Github:www.github.com/rajasekaranap